## Slide 1: RECONFIGURABLE PROCESSOR ARCHITECTURES

## Slide 2: Contents
Introduction
History
Reconfigurable Processor Architecture
Advantages and limitations
Applications

## Slide 3: INTRODUCTION

## Slide 4: The title says it all..!!!
Reconfigurable – Something that can be reconfigured or altered
Processor – An electronic circuitry that carries out the instructions of a computer program by performing the basic arithmetic, logical, control and input/output operations
Architecture – The general term to describe a physical structure

## Slide 5: Processing Circuits
Processing circuits can be broadly classified into two:
  General Purpose Processors (GPP)
  Application Specific Processors / Circuits (ASIC)

## Slide 6: A comparison between GPP and ASIC
General Purpose Processors Executes a set of instructions Performance can suffer because of fetch, decode and execute cycles Different sets of instructions can be executed and hence is highly flexible Low cost and time of development | ASIC Executes the function, the circuit is designed for Very fast and efficient execution as they are pre-tailored Can only do the function the circuit is designed for High cost and time of development

## Slide 7: Reconfigurable Processors
These come in between ASICs and GPPs
They combine the flexibility of GPP and the performance of ASIC
E.g. of RPs: FPGA, Chameleon Processor, PSoC

## Slide 8: What are Reconfigurable Processors ?
Reconfigurable processors (RP) combine the speed of application specific integrated circuits (ASIC) and the universality of general purpose processors (GPP) by means of adaptability to the currently executed code
That is, they can configure it’s internal circuitry according to the function that is being performed by the processor

## Slide 9
HISTORY

## Slide 10: A peek into history
First programmable devices
Advent of reconfigurable hardware
Reconfigurable processors

## Slide 11: First programmable hardware
First programmable devices where ROMs (Read Only Memory)
They were used to create arbitrary combinational logic functions of a number of inputs

## Slide 12: Disadvantages of ROMs
Slower than dedicated circuits
More expensive than programmable logic, especially if high speed is required
Since most ROMs do not have input or output registers, they cannot used for stand-alone for sequential logic

## Slide 13: Advent of Reconfigurable Hardware
In 1969 the first reconfigurable hardware was introduced by Motorola - XC 157, a mask-programmed gate array, with 12 gates
In 1970, Texas Instruments introduced a mask programmable IC - TMS2000 (the first PLA)

## Slide 14: Advent of Reconfigurable Hardware(contd …)
General Electric Company in 1971 developed the first erasable PLD based on programmable ROM technology
In 1975, Signetics introduced their Field Programmable Logic Array, the 82S100
Monolithic Memories in 1978 introduced the first PAL

## Slide 15: Reconfigurable Processors
Concept stated in 1960s in a paper by Gerald Estrin
Concept consisted of a main processor controlling a reconfigurable hardware
The reconfigurable hardware was tailored to perform a specific task such as image processing

## Slide 16: Reconfigurable Processors (contd …)
Altera in 1984 delivered the industry’s first reprogrammable logic device – the EP300
Xilinx invented the first commercially viable FPGA in 1985 – the XC2064

## Slide 17: Reconfigurable Processor Architecture

## Slide 18: RP architecture components
Implementation Spectrum
System Level Architecture
Granularity
Programmable Logic Elements
Reconfiguration Models

## Slide 19: 1. Implementation Spectrum
RPs can be implemented using PLDs, CPLDs and FPGAs
PLDs are only used in applications which require a very small number of gates
CPLDs are preferred where the logic circuits are to be small (<500 FFs), non-volatile and fast start-up operation
Modern day applications are usually done using FPGAs, since they support circuits of much more complexity (up to 150k FFs)

## Slide 20: 2. System Level Architecture
The system level architecture shows how the sequential processor and the RF is coupled. There are 5 different forms:
1. External standalone processing unit
2. Attached processing unit 4. Reconfigurable Functional Unit
3. Co-processor 5. Processor embedded in RF

## Slide 21: Try to add the 5 diagrams

## Slide 22: 3. Granularity
The maximum word length of the implemented functions
RFs can be categorised into two groups:
  Fine grained
  Coarse grained

## Slide 23: 3.1 Fine grained architectures
A fine-grained functional unit can typically implement a single function on a single (or small number) of bits
The most common kind of fine-grained functional units are the small lookup tables that are used to implement logic in FPGAs
Fine grained architectures are used in fast simple control applications

## Slide 24: 3.1 Fine grained architecture (contd …)
A look up table (LUT) is shown in the adjacent figure
Here we can see that there are basically 3 inputs at the top side and the output derived from these 3 inputs

## Slide 25: 3.2 Coarse grained architecture
A coarse-grained functional unit, is more larger and complicated and may consist of ALUs, MACs and possibly even a significant amount of storage.
An example is a DSP block
Coarse grained architectures are used for high bandwidth data processing like data encryption, video processing etc.

## Slide 26: 3.2 Coarse grained architecture (contd …)
The adjacent figure shows a reconfigurable unit of the ADRES architecture
Each reconfigurable functional unit in this device contains a 32-bit ALU which can be configured to implement one of several functions including addition, multiplication and logic functions and also two small register files.

## Slide 27: 4. Programmable Logic Elements

## Slide 28: Types of Reconfigurations:
Static Reconfiguration – The reconfiguration is done at the time of compilation and loading of the program E.g. FPGAs
Dynamic Reconfiguration – The reconfiguration is done during runtime E.g. Advanced Chameleon Circuits